## Slide 1: Coriolis Argo float decoder (brief description of the Matlab decoder deployed at Coriolis to decode Argo floats)
Jean-Philippe RANNOU (jean-philippe.rannou@altran.com)

## Slide 2: Matlab NKE float decoder
Two decoders for the PIs
    decode_provor_2_csv: used to generate CSV ‘raw’ decoded files
    decode_provor_2_nc: used to generate NetCDF Argo decoded files
  Usage: Delayed mode decoding of already received float data.
Two decoders for the DACs
    decode_provor_2_nc_rt: used to generate NetCDF Argo decoded files
    decode_provor_2_nc_dm: used to generate NetCDF Argo decoded files (for ProvBioII dead floats only)
  Usage: Real time mode decoding of incoming data flux.
  Decoded float versions: all Coriolis float versions ≥ PROVOR CTS3 (2010)

## Slide 3: Matlab NKE float decoder: PI decoders
Float config
Float data
PROF
TRAJ
TECH
META
CSV file
decode_provor_2_csv
decode_provor_2_nc
Matlab decoder

## Slide 4: Matlab NKE float decoder: PI decoders
Float configuration files
    _provor_floats_information_co.txt, 1 line per float
      WMO number, decoder Id, Argos/Iridium Id
      Float message size
      Cycle duration, sampling period at subsurface drift
      Misc parameter (depends on float version)
      Launch date, longitude, latitude
      Reference day (day of the first descent)
      End decoding date
    WMO_meta.json, 1 file per float
      Static meta-data
      Float configuration at launch
      Calibration coefficient (used to compute derived parameters)
      RT adjustment information
      Sensor mounted on float (ProvBioII)

## Slide 5: Matlab NKE float decoder: PI decoders
Float data files
    Argos floats
      One file of (HEX) data per cycle
      Name: ArgosId_YYYY-MM-DD-hh-mm-ss_WMO_CyNum.txt
      ArgosId: float PTT number
      YYYY-MM-DD-hh-mm-ss: date of the earlier float message of the file
      WMO: float WMO number
      CyNum: cycle number
      Ex: 117959_2015-01-09-19-39-42_6901416_007.txt
      WMO can be equal to ‘WWWWWWW’ if the ArgosId to WMO link is unknown at the time of reception of the data
      CyNum can be equal to:
      ‘EEE’: empty file (not at least one float message)
      ‘WWW’: ArgosId to WMO link is unknown at the time of reception of the data
      ‘MMM’: meta-data unavailable to compute cycle number
      ‘TTT’: test data (dated before float launch date)
      ‘GGG’: ghost messages
      ‘UUU’: cycle number value (manually) disabled by the user
      Only ‘identified’ files (i.e. with valid WMO and CyNum numbers) are processed

## Slide 6: Matlab NKE float decoder: PI decoders
Float data files
    Iridium floats
      Received mail files
      Name: co_YYYYMMDDThhmmss_IMEI_MOMSN_MTMSN_PID.txt
      YYYYMMDDThhmmss: date of the session
      IMEI: float IMEI number
      MOMSN, MTMSN numbers
      PID: PID of the process that collected the mail (unused)
      Ex: co_20130303T000948Z_300234011477800_000090_000000_11694.txt
    Rudics floats
      Collected SBD files
      Name: YYMMDD_hhmmss_FloatLoginName_CyNum.Encoding.sbd
      YYMMDD_hhmmss: date of the session
      FloatLoginName: float login name
      CyNum: cycle number
      Encoding: data encoding type (‘bin’: no encoding, ‘b64’: base 64 encoding)
      Ex: 150128_123533_lovbio049b_00016.b64.sbd or 150110_182559_lovbio082b_00000.bin.sbd

## Slide 7: Matlab NKE float decoder: PI decoders
Decoder CONFIG
label files
Matlab decoder
Decoder main configuration file
Decoder TECH
label files
Matlab core decoder
Add RTQC flags

## Slide 8: Matlab NKE float decoder: PI decoders
Decoder configuration files
    Main decoder configuration file: _prv_decoder.conf
    Decoder TECH label files (used by decode_provor_2_nc only)
      One file per decoder Id
      Name: _tech_param_name_decoderId.json
      decodeId: decoder Id
      The decoder uses the field TECH_PARAM_DEC_ID to get the right technical label name stored in the TECH_PARAM_NAME field
    Decoder CONFIG label files (used by decode_provor_2_nc only)
      One file per decoder Id
      Name: _config_param_name_decoderId.json
      decodeId: decoder Id
      The decoder uses the field CONF_PARAM_DEC_ID to get the right configuration label name stored in the CONF_PARAM_NAME field

## Slide 9: Matlab NKE float decoder: PI decoders
Matlab core decoder
get_float_info
decode_provor_argos_data
decode_provor_iridium_rudics
decode_provor_iridium_sbd
decode_provor_iridium_sbd2
create_nc_mono_prof_files
create_nc_multi_prof_file
create_nc_traj_file
create_nc_tech_file
create_nc_meta_file
Decode float data
Retrieve float information
Generate nc files